CIS 224 Software Projects: Software Engineering and Research Methods

Semester 1

Workshop 1, Thursday 5 October 2006

RHB 274, 16:00 – 18:00

Task 1

Read the following extract from the official report on the failure of the maiden flight of the Ariane 5 launcher. Try to understand as much as you can, but don’t worry if you don’t understand all the technical details.

You have 30 minutes to complete this task.

### FOREWORD

On 4 June 1996, the maiden flight of the Ariane 5 launcher ended in a failure. Only about 40 seconds after initiation of the flight sequence, at an altitude of about 3700 m, the launcher veered off its flight path, broke up and exploded. Engineers from the Ariane 5 project teams of CNES and Industry immediately started to investigate the failure.

…

The terms of reference assigned to the Board requested it

- to determine the causes of the launch failure, 
- to investigate whether the qualification tests and acceptance tests were appropriate in relation to the problem encountered, 
- to recommend corrective action to remove the causes of the anomaly and other possible weaknesses of the systems found to be at fault.

The Board started its work on 13 June 1996.

…

The report contains the analysis of the failure, the Board's conclusions and its recommendations for corrective measures, most of which should be undertaken before the next flight of Ariane 5…

### 1. THE FAILURE

#### 1.1 GENERAL DESCRIPTION

On the basis of the documentation made available and the information presented to the Board, the following has been observed:

The weather at the launch site at Kourou on the morning of 4 June 1996 was acceptable for a launch that day, and presented no obstacle to the transfer of the launcher to the launch pad. In particular, there was no risk of lightning since the strength of the electric field measured at the launch site was negligible. The only uncertainty concerned fulfilment of the visibility criteria.

The countdown, which also comprises the filling of the core stage, went smoothly until H0-7 minutes when the launch was put on hold since the visibility criteria were not met at the opening of the launch window (08h35 local time). Visibility conditions improved as forecast and the launch was initiated at H0 = 09h 33mn 59s local time (=12h 33mn 59s UT). Ignition of the Vulcain engine and the two solid boosters was nominal, as was lift-off. The vehicle performed a nominal flight until approximately H0 + 37 seconds. Shortly after that time, it suddenly veered off its flight path, broke up, and exploded. A preliminary investigation of flight data showed:

- nominal behaviour of the launcher up to H0 + 36 seconds;

- failure of the back-up Inertial Reference System followed immediately by failure of the active Inertial Reference System;

- swivelling into the extreme position of the nozzles of the two solid boosters and, slightly later, of the Vulcain engine, causing the launcher to veer abruptly;

- self-destruction of the launcher correctly triggered by rupture of the links between the solid boosters and the core stage.

The origin of the failure was thus rapidly narrowed down to the flight control system and more particularly to the Inertial Reference Systems, which obviously ceased to function almost simultaneously at around H0 + 36.7 seconds.

#### 1.2 INFORMATION AVAILABLE

The information available on the launch includes:

- telemetry data received on the ground until H0 + 42 seconds 
- trajectory data from radar stations 
- optical observations (IR camera, films) - inspection of recovered material.

…

#### 1.3 RECOVERY OF MATERIAL

The self-destruction of the launcher occurred near to the launch pad, at an altitude of approximately 4000 m. Therefore, all the launcher debris fell back onto the ground, scattered over an area of approximately 12 km2 east of the launch pad. Recovery of material proved difficult, however, since this area is nearly all mangrove swamp or savanna.

Nevertheless, it was possible to retrieve from the debris the two Inertial Reference Systems. Of particular interest was the one which had worked in active mode and stopped functioning last, and for which, therefore, certain information was not available in the telemetry data (provision for transmission to ground of this information was confined to whichever of the two units might fail first). The results of the examination of this unit were very helpful to the analysis of the failure sequence.

### …

### 2. ANALYSIS OF THE FAILURE

#### 2.1 CHAIN OF TECHNICAL EVENTS

In general terms, the Flight Control System of the Ariane 5 is of a standard design. The attitude of the launcher and its movements in space are measured by an Inertial Reference System (SRI). It has its own internal computer, in which angles and velocities are calculated on the basis of information from a "strap-down" inertial platform, with laser gyros and accelerometers. The data from the SRI are transmitted through the databus to the On-Board Computer (OBC), which executes the flight program and controls the nozzles of the solid boosters and the Vulcain cryogenic engine, via servovalves and hydraulic actuators.

In order to improve reliability there is considerable redundancy at equipment level. There are two SRIs operating in parallel, with identical hardware and software. One SRI is active and one is in "hot" stand-by, and if the OBC detects that the active SRI has failed it immediately switches to the other one, provided that this unit is functioning properly. Likewise there are two OBCs, and a number of other units in the Flight Control System are also duplicated.

The design of the Ariane 5 SRI is practically the same as that of an SRI which is presently used on Ariane 4, particularly as regards the software.

Based on the extensive documentation and data on the Ariane 501 failure made available to the Board, the following chain of events, their inter-relations and causes have been established, starting with the destruction of the launcher and tracing back in time towards the primary cause.

- The launcher started to disintegrate at about H0 + 39 seconds because of high aerodynamic loads due to an angle of attack of more than 20 degrees that led to separation of the boosters from the main stage, in turn triggering the self-destruct system of the launcher.

- This angle of attack was caused by full nozzle deflections of the solid boosters and the Vulcain main engine.

- These nozzle deflections were commanded by the On-Board Computer (OBC) software on the basis of data transmitted by the active Inertial Reference System (SRI 2). Part of these data at that time did not contain proper flight data, but showed a diagnostic bit pattern of the computer of the SRI 2, which was interpreted as flight data.

- The reason why the active SRI 2 did not send correct attitude data was that the unit had declared a failure due to a software exception.

- The OBC could not switch to the back-up SRI 1 because that unit had already ceased to function during the previous data cycle (72 milliseconds period) for the same reason as SRI 2.

- The internal SRI software exception was caused during execution of a data conversion from 64-bit floating point to 16-bit signed integer value. The floating point number which was converted had a value greater than what could be represented by a 16-bit signed integer. This resulted in an Operand Error. The data conversion instructions (in Ada code) were not protected from causing an Operand Error, although other conversions of comparable variables in the same place in the code were protected.

- The error occurred in a part of the software that only performs alignment of the strap-down inertial platform. This software module computes meaningful results only before lift-off. As soon as the launcher lifts off, this function serves no purpose.

- The alignment function is operative for 50 seconds after starting of the Flight Mode of the SRIs which occurs at H0 - 3 seconds for Ariane 5. Consequently, when lift-off occurs, the function continues for approx. 40 seconds of flight. This time sequence is based on a requirement of Ariane 4 and is not required for Ariane 5.

- The Operand Error occurred due to an unexpected high value of an internal alignment function result called BH, Horizontal Bias, related to the horizontal velocity sensed by the platform. This value is calculated as an indicator for alignment precision over time.

- The value of BH was much higher than expected because the early part of the trajectory of Ariane 5 differs from that of Ariane 4 and results in considerably higher horizontal velocity values.

The SRI internal events that led to the failure have been reproduced by simulation calculations. Furthermore, both SRIs were recovered during the Board's investigation and the failure context was precisely determined from memory readouts. In addition, the Board has examined the software code which was shown to be consistent with the failure scenario.

Therefore, it is established beyond reasonable doubt that the chain of events set out above reflects the technical causes of the failure of Ariane 501.

#### 2.2 COMMENTS ON THE FAILURE SCENARIO

In the failure scenario, the primary technical causes are the Operand Error when converting the horizontal bias variable BH, and the lack of protection of this conversion which caused the SRI computer to stop.

It has been stated to the Board that not all the conversions were protected because a maximum workload target of 80% had been set for the SRI computer. To determine the vulnerability of unprotected code, an analysis was performed on every operation which could give rise to an exception, including an Operand Error. In particular, the conversion of floating point values to integers was analysed and operations involving seven variables were at risk of leading to an Operand Error. This led to protection being added to four of the variables, evidence of which appears in the Ada code. However, three of the variables were left unprotected. No reference to justification of this decision was found directly in the source code. Given the large amount of documentation associated with any industrial application, the assumption, although agreed, was essentially obscured, though not deliberately, from any external review.

The reason for the three remaining variables, including the one denoting horizontal bias, being unprotected was that further reasoning indicated that they were either physically limited or that there was a large margin of safety, a reasoning which in the case of the variable BH turned out to be faulty. It is important to note that the decision to protect certain variables but not others was taken jointly by project partners at several contractual levels.

There is no evidence that any trajectory data were used to analyse the behaviour of the unprotected variables, and it is even more important to note that it was jointly agreed not to include the Ariane 5 trajectory data in the SRI requirements and specification.

Although the source of the Operand Error has been identified, this in itself did not cause the mission to fail. The specification of the exception-handling mechanism also contributed to the failure. In the event of any kind of exception, the system specification stated that: the failure should be indicated on the databus, the failure context should be stored in an EEPROM memory (which was recovered and read out for Ariane 501), and finally, the SRI processor should be shut down.

It was the decision to cease the processor operation which finally proved fatal. Restart is not feasible since attitude is too difficult to re-calculate after a processor shutdown; therefore the Inertial Reference System becomes useless. The reason behind this drastic action lies in the culture within the Ariane programme of only addressing random hardware failures. From this point of view exception - or error - handling mechanisms are designed for a random hardware failure which can quite rationally be handled by a backup system.

Although the failure was due to a systematic software design error, mechanisms can be introduced to mitigate this type of problem. For example the computers within the SRIs could have continued to provide their best estimates of the required attitude information. There is reason for concern that a software exception should be allowed, or even required, to cause a processor to halt while handling mission-critical equipment. Indeed, the loss of a proper software function is hazardous because the same software runs in both SRI units. In the case of Ariane 501, this resulted in the switch-off of two still healthy critical units of equipment.

The original requirement acccounting for the continued operation of the alignment software after lift-off was brought forward more than 10 years ago for the earlier models of Ariane, in order to cope with the rather unlikely event of a hold in the count-down e.g. between - 9 seconds, when flight mode starts in the SRI of Ariane 4, and - 5 seconds when certain events are initiated in the launcher which take several hours to reset. The period selected for this continued alignment operation, 50 seconds after the start of flight mode, was based on the time needed for the ground equipment to resume full control of the launcher in the event of a hold.

This special feature made it possible with the earlier versions of Ariane, to restart the count- down without waiting for normal alignment, which takes 45 minutes or more, so that a short launch window could still be used. In fact, this feature was used once, in 1989 on Flight 33.

The same requirement does not apply to Ariane 5, which has a different preparation sequence and it was maintained for commonality reasons, presumably based on the view that, unless proven necessary, it was not wise to make changes in software which worked well on Ariane 4.

Even in those cases where the requirement is found to be still valid, it is questionable for the alignment function to be operating after the launcher has lifted off. Alignment of mechanical and laser strap-down platforms involves complex mathematical filter functions to properly align the x-axis to the gravity axis and to find north direction from Earth rotation sensing. The assumption of preflight alignment is that the launcher is positioned at a known and fixed position. Therefore, the alignment function is totally disrupted when performed during flight, because the measured movements of the launcher are interpreted as sensor offsets and other coefficients characterising sensor behaviour.

Returning to the software error, the Board wishes to point out that software is an expression of a highly detailed design and does not fail in the same sense as a mechanical system. Furthermore software is flexible and expressive and thus encourages highly demanding requirements, which in turn lead to complex implementations which are difficult to assess.

An underlying theme in the development of Ariane 5 is the bias towards the mitigation of random failure. The supplier of the SRI was only following the specification given to it, which stipulated that in the event of any detected exception the processor was to be stopped. The exception which occurred was not due to random failure but a design error. The exception was detected, but inappropriately handled because the view had been taken that software should be considered correct until it is shown to be at fault. The Board has reason to believe that this view is also accepted in other areas of Ariane 5 software design. The Board is in favour of the opposite view, that software should be assumed to be faulty until applying the currently accepted best practice methods can demonstrate that it is correct.

This means that critical software - in the sense that failure of the software puts the mission at risk - must be identified at a very detailed level, that exceptional behaviour must be confined, and that a reasonable back-up policy must take software failures into account.